## Slide 1
OSC48Mhz -FLL
Richard Morisson 27 February 2026

## Slide 2
Summary :
ELMOS Requirement and Definition main parameters
OSC 48M Ramp :Results and Drawbacks
FLL Architecture description and advantages
Optimization Tc_ppm/k equivalent for REQ * C
5imulation Tc_ppm/k Req * C
Description and simulation internal block : Rtimm , OPAMP,VCO
PVT TOP OSC48MFLL Simulations and summary
First draft simulation selectable OSC48MFLL/OSC64MFLL !!

## Slide 3: ELMOS MAIN Requirements in KEY FOUNDRY HVT : Design a High Precision 48 Mhz OSCILLATOR with a minimum Error after trimming . I define 3 specification ranges : 1) Specification 1 ( nominal) : Vdd: 1.35 to 1.65 V , Temp :-40 to +160dC , with ERROR <<+/-1% 2) Specification 2 : Vdd: 1.35V to 1.65V , Temp :-55 to +175dC , with ERROR < +/-1% 3) Specification 3 : Vdd: 1.25V to 1.65V , Temp :-55 to +175dC ,with ERROR ≈ +/-1% Design Priorities : 1) Minimizing Error with Robust Design 2) Power Consumption 3) Layout Area
Definition ERROR % : Error +/- % = 50( Fout(MAX) –Fout(MIN))/Fout(Average)
Fout measured with three supply voltage and full temperature range .
Two other parameter are also given :
PSRR(dB) = db20 (( Fout(Vdd max)/Fout(Vdd min))-1) /( (Vddmax/Vddmin)-1)
calculated for each temperature step
TC_ppm/K = 1e6 *( Fout(max)-Fout(min))/((Fout(average)* Temp(max)-Temp(min))
Calculated for each Vdd step
TEMP
Fout
Vdd(Typ)
Vdd(Min)
Vdd(Max)
Fout(Average))
Fout(max)
Fout(min)

## Slide 4: Existing Design in KEY Foundry : OSC48M Architecture Relaxation ramp :

## Slide 5
CURRENT
MIRROR
CURRENT
MIRROR
iref
Irampe irampe
C1
C2
C1
C2
icomp
icomp
Rref
Trimming
Fosc
IBIAS
(5ua)
OFFA
Ready
FOSC
CompJK
CompJK
DTC
VREF
FTRIM<0:7>
VDD(1.5V)
ISO (5V)
Capacitors
Array
GND
PSUB
Trimming
VREF
RTRIM<0:3>
0.35V
ATB_SEL<0:7>
ATB_MUX (5V)
ATB0
ATB1
ATB0_EN
ATB1_EN
and
and
AVDD
(5V)
BLOCK DIAGRAM OSC48M

## Slide 6: Existing Design in KEY Foundry : OSC48M main result

## Slide 7: OSC48M LIMITATIONS : 1) Relaxation based on equivalent Resistance Rref with capacitance C1(or C2): Fosc=1/(2 Rref *C1) (excluding delai comparator) Rref resistance Rdppo_ns ( width=2um) Capacitance : realized with cmom capacitance array ( trimming) as Rref *C1 is not constant versus temperature Fosc will not be constant . 2) second order effect : Comparator delai which is not constant versus temperature and supply Oscillation frequency will be Fosc = 1/(2Rref*C1+2 Td) If Fosc is small << 10 Mhz Td could be neglected here for Fsoc=48Mhz Td will impact PSRR ,Tc_ppm/K and Error +/- %

## Slide 8: New Architecture : FLL OSCILLATOR
TRIMMING
Fosc
512
-
+
GND
PSUB
OFFA
FTRIM<0:8>
VDD (1.5V+/-10%)
F48M
R
ISO
VREF (0.9V)
S
Sn
Sn
S
VRES
C1
C1
C2
Rf
Rf
Cf
Cf
+ -
OPAMP
VCO
VSC
%2
%2
%2
%2
96Mhz
24Mhz
12Mhz
6Mhz
S
Sn
nmos5V
nmos5V
nmos5V
nmos5V
VCCA(5V)
IRES
F24M
F12M
F6M
Cg
GND
START
Bandgap
VREF+IREF
OFFA
VCP=3VDD
MIN
MAX
Duty
Cycle
DTC
Ready
READY
ATB0_EN
ATB1_EN
ATBSEL<0:7>
ATB_MUX
ATB0
ATB1
VDD
48Mhz
OFFA
VCP
48Mhz
Charge
Pump
Level
Shift

## Slide 9: FLL ARCHITECTURE PRINCIPLE : Steady state loop : VSC(average)=VRES
VRES
S=1
Sn=1
VSC
+
-
VCO
(96Mhz)
Divider / 16
VSC
VRES
Fosc(6Mhz)=1/(2 T)
Fosc(48M) ≈ 8/(2*Req*C1) with C2>>C1 , Req will be trimmed to get the proper oscillation frequency
LP
Filter
T=Req*C1
VC
VCf
Fout=VCf*Kvco

## Slide 10: Why FLL ARCHITECTURE ? 1) FLL :Frequency LOCK LOOP Main avantage : it is a closed loop design so internal block delais do not any impact oscillation frequency versus temperature and supply ( no Td impact as previous architecture ramp) . By construction PSRR (dc) should be neglectable 2) Remain the time constant T= Req * C which should be constant versus temperature and supply Vdd . Key Foundry provide a resistance (Rdppo_ns) which coefficient of temperature Tc1 dépend of width ! The goal is to get Res*C with the lowest Tc_ppm/K !

## Slide 11: Model Req*C with excell file : optimum width resistance 4.5um Tc_ppm/k (-40..+175dc)= 31.45 !!

## Slide 12: Design OSCM48 FLL
Bandgap
Switch/Cap
Trimm
Res
LP
Filter
OPAMP
VCO
ATB_MUX
TEST
MIN/MAX
Mirror nmos
Mirror
pmos
Charge
Pump
Test
Duty
READY
Start OSC
ON/OFF dc

## Slide 13: Simulation Validation Time constante :T=Req*C
Emulation Time constant by measuring in DC and AC ;Req and C versus Temperature and VDD
Emulation Req (DC)
Emulation Switch Cap (AC)

## Slide 14: Results simulation , process TTT ( trimmed code to get Fsoc=48Mhz) Temp:-55 to 175dC , Vdd:1.25 to 1.65V
Emulation Req (DC)
Emulation Switch Cap (AC)

## Slide 15: Resistance with trimming 9 bits
Emulation Req (DC)
Step :32 LSB
Step :1 LSB around Fosc=48Mhz
Step : TTT 100khz SSS 130khz, FFF: 70khz

## Slide 16: OPAMP :classical two stages OTA
Emulation Req (DC)

## Slide 17: OPAMP Characteristics
Emulation Req (DC)

## Slide 18: VCO : V/I amplifier loading ring oscillator providing 96Mhz Followed by divider 2 to 16 .
Emulation Req (DC)
V/I amplifier
V/I amplifier
Delay Cell
Delay Cell

## Slide 19: VCO : Simulation PVT results versus Vc (Centered at VREF=0.9V)
Emulation Req (DC)
V/I amplifier
V/I amplifier
Delay Cell
Delay Cell

## Slide 20: Bandgap:providing current 10uA (VCO,OPAMP) and VREF=0.9V (to VCO) (Reused OSC32MCCO)
V/I amplifier
V/I amplifier
Delay Cell

## Slide 21: Bandgap simulation results versus PVT :temp-55 to 175, Vdd 1.25 to 1.65 , all corners
V/I amplifier
V/I amplifier
Delay Cell

## Slide 22: Charge PUMP +Translator : loading Switch Cap : . Why Charge pump ? Reduce RON SWITCH ( REQ=Cste) (switch Vdd=1.25 mos 1.5V don’t work)
V/I amplifier
V/I amplifier
Delay Cell
Charge Pump
TRanslator
Switch Cap
Two Stages Dickson
Dickson
TRanslator

## Slide 23: TOP SIMULATION RESULTS VERSUS PVT (Results simulation 28 Feb) All corners trimmed at Vdd=1.5V and Temp=40dC
V/I amplifier
V/I amplifier
Delay Cell

## Slide 24: Summary Specification parameter (after trimming)
V/I amplifier
V/I amplifier
Delay Cell
PARAMETERS | MIN | MAX | AVERAGE | STDEV | COMMENT
FOSC (Mhz) (with Trimming) | 47.44 | 48.212 | 47.91 | 0.174 | SPEC3
I_ON (uA) | 266 | 442 | 332 | 41 | SPEC3
ERROR +/- % | 0.44 | 0.67 | 0.53 | 0.091 | SPEC 3
ERROR +/- % | 0.43 | 0.63 | 0.5 | 0.085 | SPEC 2
ERROR +/- % | 0.332 | 0.444 | 0.368 | 0.047 | SPEC 1
TC_ppm/K | 28 | 43.3 | 33.1 | 4.8 | SPEC1
PSRR (dB) | -64 | -44 | -51 | 4 | SPEC1
Step Trimm (kHz) (around 48Mhz) | 70 | 130 | 100 | 10 | SPEC3
Duty Cycle (48Mhz) | 0.4956 | 0.5054 | 0.499966 | 0.0017 | SPEC3

## Slide 25: Going to 64 Mhz OSCILLATOR ? Only two small changes :  increasing the current loading the switch cap by 33%  increasing the current in the VCO by 33% These two changes could be easily digitally control (1bit) meaning that the IP could provide 48Mhz and 64Mhz ..with the same trimmed values !!
V/I amplifier
V/I amplifier
Delay Cell
Digital Current control for Switch Cap
Digital Current control for VCO (ZOOM)

## Slide 26: First simulation with bit control SEL48M : All corner (trimmed) , Temp=40dC, Vdd=1.5V
V/I amplifier
Delay Cell
V/I amplifier